# Tomco Service Bulletin

# For Technicians by Technicians

# Volume 1, Issue 2	February 7, 2002

# Text boxes

BEWARE THE HALLOWED GROUND!

One of our Distributors asked why we have more 4 wire universal O2 Sensors than our Competition.  Vehicle Manufacturers use two ways to ground their 4 wire O2 Sensors.

- Body Grounded Sensor - the ceramic cell is grounded directly to the body of the sensor.

- Dedicated Ground Sensor - the cell is not grounded to the body, but directly to the Computer.

"So what" you say !!!  Well the O2 ground is very important to how the Computer sees or reads the signal.  If you install a dedicated ground sensor in a body grounded application the computer may not be able to read the sensor voltage correctly.  This will result in driveability problems.

A major manufacturer was supplying a dedicated ground sensor to replace a body grounded sensor.  This sensor would not work correctly in this application.

At Tomco we match the correct OE grounding type for each particular application, so you won't have this problem.  Also when you sell a universal O2 sensor,  make sure what style grounded sensor you have.  That is why Tomco has more than one style of 4 wire universal  O2 sensor.

So sell your customer what he needs - The right part - TOMCO!

John

We Support